## Slide 1: Complex object manipulation with hierarchical optimal control
Dr. Alex Simpkins and
Prof. Emanuel Todorov
University of Washington, Seattle

## Slide 2: Object Manipulation
Controlling the trajectory or state of an object with external forces applied by manipulators
Complex problem
  Nonlinearities
  Contacts/collisions
    Discontinuities
    Changing problem
  Friction
  Redundancy
  High dimensionality
  Under-actuation
Notes: How can we deal with these issues from a control and reinforcement learning perspective? Well the dimensionality is massive, so classical methods won’t easily work here (without a super computer and years to solve the problem).

## Slide 3: Object Manipulation
Significance/Relevance
  Interaction with the world is part of learning and normal functioning
    We explore and process Haptic information, expand knowledge
    Better method, improved learning
  Humans are excellent at interacting dynamically with our dynamic world!
    This is poorly understood from a control/machine learning perspective
      Crumple a piece of paper 60 times, you will do it 60 different ways
  Significant portion of neurons in brain involved in sensorimotor processes
  Artificial systems need to interact with the world intelligently
Notes: Weight, shape, texture, color, surface properties, rigidity, elasticity, etc
Dangerous environments, adaptability, human-machine interaction

## Slide 4: Existing approaches
Manipulation
  Assume a grip predefined, contacts static/quasi-static
  Determine forces to move object in prescribed manner
  Optimal control
Grasp studies – how do humans grasp objects?
  Quasi-static notion yet again
Locomotion approaches
  Manipulation and locomotion are highly related
    Many of the challenges are similar
  Relevant locomotion approaches which are promising based upon optimal control and RL
    Typically hierarchical, often offline components
[Popovic]
[Liu]
[Popovic]

## Slide 5: Model
2D – first step
Objects
  Mass, center of mass, inertia, boundary
Given # of manipulators
  Modeled as point masses, since actuators are very capable, and dynamics are approximately linear (dominated by rotor J)
Simple/efficient/fast contact/collision algorithm here
  No-slip condition (equivalent to very sticky objects/manipulator end points)
  Facilitates realtime implementation
    Parallel GPU processing possible
2-part computation - total forces on
  Object
  Manipulators (contact or not)
Notes: Question about move to reality, and answer is MPC is forgiving to modeling errors because of feedback, and biological systems do not have perfect models, but operate instead under uncertainty quite effectively, through feedback
Dimensionality note – 5 states per manipulator, plus 4 states of object – I solved this for up to 10 manipulators in realtime, 54 dimensions without significant issue with non-optimized code in matlab (eg running graphics updates, not vectorizing absolutely everything, etc) – most of what you see today is a mere 19 dimensions, which is still large

## Slide 6: Hierarchical control methodology
Break up single complex problem into multiple more tractable problems
Hierarchical – allows different strategies at each stage, more freedom
Behaviors can be encoded at various levels
Notes:   MPC or Feedback
    Low-D so easier/fast to implement MPC
    P/PD/PID alternative for early prototyping
Complex behaviors from simple control policies

## Slide 7: Force-Cost function
Mid-Level
  Given required force, and the state of the system
    What should the individual forces be?
    Where should they be applied?
  Optimization and FC function
    Part I : Arranged as quadratic optimization, terms account for
      Force tracking error
      Minimizing individual forces
    Part II : Virtual force field, similar to a cost function
      State of system, workspace of each manipulator, location of end effector, location and parameters (or estimated) of object
Notes: Getting to target given some state of the system
2) Applying some force to object
3) Distribution of contact points
4) Desire to change contact points (break contact) whenappropriate
5) Handle limited workspace
6) What to do if an object moves outside of theworkspace, or the end effector moves outside theworkspace
First term pulls finger toward object surface, decreases as further from center of workspace
Second term pulls finger away from the surface of the object – larger the further from the center of the workspace the finger is, decreases as gaussian function of distance from center of object

## Slide 8: Experimental tasks
Given a # of end effectors, manipulate an object of known parameters
  Grab object, then track some reference for the object
  Perform continuous rotation of the object in place
  In both cases manipulator bases are fixed
    Everything happens due to manipulators, not an arm

## Slide 9: Results – force tracking

## Slide 10: Results – grasp and track
a

## Slide 11: Results – contact breaking

## Slide 12: Conclusions
Contributions
  New dynamic hierarchical control approach to manipulation, also applicable to locomotion
  Minimal manual tweaking (as opposed to some ‘painful’ methods), tuned with intuitive parameters (only a few), easy to expand behavioral complexity or blend/change behaviors online
  Realtime implementation – no offline computation, fast enough to run on real robots
  Manipulation and locomotion treated as the same problem
  Joint limit handling with soft boundary acting as a spring when moving outside workspace, contributes to numerical stability, smoothness, parallels biological systems
In progress/next steps
  3D
  Implementation on real robots (object spinning task)
  MPC at lower level vs. force fields (comparison)
  Stability/robustness analysis more quantitative
  Active sensing – learn object while manipulating, or manipulate to learn object
  Compare with trajectory methods, also being developed in our lab

## Slide 13: Thank you
More information at casimpkinsjr.radiantdolphinpress.com

## Slide 14: Appendix - 1
Ease of tuning – high level doesn’t affect low level stability
  Build stable system in pieces if necessary with difficult systems